## Slide 1
Smart-REPLIC
Reliable UDP in C, with a neural network that learns congestion control
Computer Networks | Faculty: Anuradha G | VIT Vellore
Harshavardhan Mallela 24BAI0274 Rohit Arya 24BCE0819 Shloak Sinha 24BDS0378

## Slide 2
WHY
UDP is fast but unreliable; TCP is reliable but locked in the kernel
2 / 26
UDP
Fast and simple. Packets can be lost, duplicated or reordered, and nothing tells the sender.
TCP
Reliable, but it lives inside the operating system: hard to see, hard to change, hard to learn from.
Our question
Can we rebuild the core ideas of TCP ourselves on top of UDP, in a form we can read, tune and teach a neural network to control?
QUIC and HTTP/3 take the same route: reliability built in user space over UDP.

## Slide 3
WHAT WE BUILT
A complete system: protocol, learned controller, network and tools
3 / 26
REPLIC protocol
Handshake, Selective Repeat, CRC-16, adaptive timer. About 470 lines of C in the core.
Smart-REPLIC controller
A 5-32-32-5 neural network picks the window; safety net hands over to AIMD when loss is high.
Network design
Four routers, OSPF, VLANs and an ACL in Cisco Packet Tracer, with failover.
Applications and tools
Terminal and web chat, REPLIC Drop file race, Wireshark dissector, a C library.
A student on VLAN 10 uploads a file to the server LAN. The ACL blocks staff VLAN 20. If a core link fails, OSPF reroutes through R2 and the transport adapts to the longer path.

## Slide 4
RESULTS
The neural agent beats tuned AIMD on every kind of path we tested
4 / 26
15% to 52%
less time than tuned AIMD on 4 of 5 paths (real clock, 10 paired runs)
65% to 83%
less time on the real Linux kernel (netem), significant on three paths
0.53x
the time of tuned AIMD across 100 random held-out paths; faster on 89
4 of 4
paths that change mid-transfer: neural agent fastest in every case
0.84 vs 0.64
Jain fairness with unequal RTTs, neural against AIMD
24% to 34%
link share next to a kernel TCP flow: it does not starve TCP
The same trained network is used in every test, with no retuning. Opponents are tuned AIMD and tuned CUBIC, not weak baselines.

## Slide 5
RESULTS
Up to 83% less time than tuned AIMD
5 / 26
Chart: Completion time saved against tuned AIMD (%)
| 5G-like | Lossy 2% | Satellite-like
Real clock, emulated paths | 15 | 49 | 52
Real Linux kernel (netem) | 65 | 71 | 83
Same trained network on every path
Real clock: 10 paired runs per path, 95% intervals
Kernel: 3 to 5 runs per cell, all three significant
Also 52% on the fast path, and 0.53x on 100 random paths

## Slide 6
RESULTS
Compared with every alternative we built or measured
6 / 26
Alternative | Where measured | Neural agent result
Tuned AIMD | Real clock; real kernel | 15% to 52% less time (real clock); 65% to 83% (kernel)
AIMD, window 32 | Real clock; 2 MB file | Faster on every path; 2 MB lossy file 11.9 s vs 26.6 s
CUBIC (tuned) | Real clock, 10 paired runs | Faster on lossy (-74%) and satellite (-34%); equal on 5G and fast
BBR-style | Virtual time, 20 seeds | Wins satellite and fast; level on 5G; BBR-style wins lossy
Q-table agent | C transport, 15 runs | Table agent slower than AIMD on 5G and satellite; neural wins all three
Plain UDP | 48 simulated paths | Plain UDP delivered 68% of packets; REPLIC delivers all
Kernel TCP (what FTP and SCP run on) | Real Linux kernel, netem | TCP is 1.5x to 1.7x faster than the neural agent, which is 3x to 6x faster than REPLIC with AIMD
FTP and SCP run on kernel TCP, so the kernel TCP row is the comparison; we did not run an FTP client itself.

## Slide 7
RESULTS
Real clock: fastest on four of five paths against tuned baselines
7 / 26
Chart: Completion time (s), lower is better
| 5G-like | Lossy 2% | Satellite | Fast | Hostile 10% loss
AIMD window 32 | 1.41 | 7.98 | 17.93 | 14.55 | 7.54
AIMD tuned | 1.09 | 7.05 | 11.36 | 8.2 | 8.34
CUBIC tuned | 1.19 | 13.92 | 8.26 | 6.52 | 12.32
Neural agent | 0.92 | 3.62 | 5.46 | 3.92 | 8.93
Neural agent fastest on 4 of 5 paths, significantly faster than tuned AIMD on all four
Faster than tuned CUBIC on lossy (-74%) and satellite (-34%)
Hostile 10% loss: no significant difference between any two policies
Real clock, real server process; 10 paired runs per path (hostile: 5), 95% intervals

## Slide 8
RESULTS
Why it wins: it rides a higher window and backs off only on loss
8 / 26
Same lossy path, same seed, same transport
AIMD (grey) saws between 5 and 15 packets and needs 9 s
The agent (green) holds a much larger window, backs off on loss, and finishes in 4 s

## Slide 9
RESULTS
On the real Linux kernel: 2.5x to 6x faster than AIMD, within 1.5x to 1.7x of TCP
9 / 26
Chart: Mean completion time (s), 500 packets of 512 bytes, lower is better
| Lossy 2% | 5G-like | Satellite | Reordering
Kernel TCP | 0.88 | 0.28 | 1.91 | 0.94
REPLIC AIMD tuned | 4.75 | 1.23 | 16.72 | 4.06
REPLIC neural agent | 1.35 | 0.43 | 2.92 | 1.64
Linux tc/netem on loopback, 5 runs per cell (satellite 3)
Neural agent beats tuned AIMD by 65% to 83%; significant on three paths, reordering not
Kernel TCP is faster than any user-space REPLIC policy, as expected
Next to a kernel TCP flow our agent takes 24% to 34% of the link

## Slide 10
RESULTS
When the path changes mid-transfer, the neural agent is fastest every time
10 / 26
Chart: Mean completion time (s), virtual time, 20 paired seeds
| Bandwidth drop | Bandwidth rise | Delay jump | Hand-over pattern
AIMD tuned | 13.6 | 9.2 | 33.3 | 12.8
CUBIC | 17.7 | 15.1 | 27.5 | 21.4
BBR-style | 13.4 | 5 | 25.9 | 10.8
Neural agent | 12.7 | 4.3 | 19.8 | 8.2
4 of 4 changing-path cases: neural fastest
Cost: 1% to 6% retransmissions
The BBR-style baseline beats tuned AIMD on 4 of 5 named paths, so this is a strong opponent
Simplified BBR in virtual time; not the Linux BBR

## Slide 11
RESULTS
Fair between neural flows, and it does not starve kernel TCP
11 / 26
Chart: Share of the link next to a kernel TCP flow (%)
| 5G-like | Lossy 2% | Satellite
Neural agent | 24 | 30 | 34
Tuned AIMD | 8 | 16 | 5
Two identical flows | Extra RTT | Share short-RTT | Jain
AIMD / AIMD | 150 ms | 88% | 0.64
Neural / neural | 150 ms | 71% | 0.84
TCP keeps the rest of the link in every case
Neural flows are fairer than AIMD under unequal RTTs; the short-RTT flow still wins more
Coexistence: 3 runs per cell on one laptop, so shares are good to about ten points

## Slide 12
RESULTS
It works between two real machines over the internet
12 / 26
Chart: First clean repetition, completion time (s)
| Kernel TCP | AIMD | CUBIC | BBR-style | Neural agent
Rep 1, 2 MB | 2.47 | 14.23 | 12.44 | 6.35 | 4.7
Two laptops on different networks, Tailscale relay, about 79 ms round trip; 2 MB per transfer, 5 repetitions
Every completed REPLIC transfer delivered 4,000 of 4,000 packets
Rep 1: neural 4.7 s, BBR-style 6.4 s, AIMD 14.2 s, kernel TCP 2.5 s
The relayed path drifted (TCP alone took 2 s to 51 s) and 4 of 20 runs timed out, so no ranking is claimed from reps 3 to 5

## Slide 13
DEMO
REPLIC Drop: race the policies on any file
13 / 26
Drop in any file (up to 12 MB), pick a network, race AIMD 32, tuned AIMD and the neural agent
Example, 2 MB on lossy Wi-Fi: neural 13.0 s, AIMD 26.7 s, tuned AIMD 29.5 s (one run each)
Each received copy is checked byte for byte (SHA-256) and can be downloaded
Real C stack: libreplic sender, bin/server and the bin/impair proxy; make drop starts it

## Slide 14
DEMO
REPLIC Chat: two people, two machines, over the internet
14 / 26
Every message is a REPLIC segment; ACKs and retransmissions are visible in the live counters
Two machines linked over Tailscale; works across the internet
Window controller switch: fixed window, AIMD or Smart-REPLIC
Loss slider shows the protocol recovering in real time

## Slide 15
DEMO
Network design in Packet Tracer: OSPF, VLANs, ACL and failover
15 / 26
4 routers, OSPF area 0; 2 VLANs with router-on-a-stick and DHCP
Student PCs are blocked from staff VLAN 20 by an ACL
Failover: shutting R1 Gi0/2 reroutes through R2; 70 of 71 pings still succeed
Packet Tracer cannot run C programs, so protocol and network are validated separately

## Slide 16
DEMO
Wireshark: a custom dissector decodes REPLIC
16 / 26
Dissector network/replic.lua decodes seq, ack, flags and CRC. Left: the 3-way handshake. Right: filtering one sequence number shows its retransmissions.

## Slide 17
HOW IT WORKS
REPLIC: a 13-byte header, a three-way handshake and a CRC on every packet
17 / 26
seq
4 B
ack
4 B
flags
1 B
crc
2 B
len
2 B
payload up to 512 B
SYN
Client to server
Request a connection
SYN-ACK
Server to client
Server agrees
ACK
Client to server
Established; data flows
DATA / ACK
Both ways
Window of packets in flight
FIN
Either
Close the connection
Packets are numbered, acknowledged and checksummed; a corrupt packet is dropped and recovered by retransmission.

## Slide 18
HOW IT WORKS
Selective Repeat: resend only what is missing
18 / 26
Receiver buffers out-of-order packets (256-packet window) and reports them in a 32-byte bitmap in every ACK
Sender keeps one timer per packet; adaptive timeout with a floor of 1.3 x smoothed RTT
About 10x fewer retransmissions than Go-Back-N
Web chat, 200 messages: 6.4 s against 11.9 s with AIMD
Go-Back-N kept for comparison (--gbn)
C transport (s) | AIMD 32 | Neural | Gain
5G-like | 1.27 | 1.16 | 9%
Lossy 2% | 7.99 | 4.29 | 46%
Satellite-like | 25.7 | 12.9 | 50%
Hostile 10% loss | 7.3 | 8.1 | tie
10 runs per cell, 95% intervals; all gains significant except the hostile row.

## Slide 19
HOW IT WORKS
Five congestion controllers behind one interface
19 / 26
AIMD
Add 1 per RTT, halve on loss. The TCP Reno idea.
CUBIC
Window grows as a cubic curve after loss.
BBR-style
Estimates bandwidth and RTT; paces at the estimate.
Q-table
Small learned table of window actions.
Neural agent
5-32-32-5 network, 1,413 weights, picks the window multiplier.
Inputs: four measured values (RTT growth, loss, throughput share, window) plus the last action
Five actions: multiply the window by 0.5, 0.85, 1.0, 1.15 or 1.5
Window cap 128, slow start to 64, pacing at 2 x window / RTT
Safety net: AIMD takes over while an interval loses 10% or more

## Slide 20
HOW IT WORKS
What matters: window cap 128, pacing, slow start and the timer floor
20 / 26
Chart: Ablation, 100 random held-out paths (lower is faster)
| Tuned AIMD | Neural, final | no slow start | no pacing | no hand-over | cap 32 | no timer floor | original settings
Time relative to tuned AIMD | 1 | 0.51 | 0.527 | 0.549 | 0.506 | 0.837 | 0.519 | 0.859
100 random paths: neural 0.53x the time of tuned AIMD, faster on 89, never more than 20% slower
Removing the cap 128 or using the original settings loses most of the gain
Evolution-strategy retraining in C added only 2%: not adopted

## Slide 21
TESTING
How we tested: correctness first, then four steps toward the real world
21 / 26
1 Emulation in the client
Fast, repeatable; also virtual time (1000x faster, matches the real clock in 15 of 15 cells)
2 Impairment proxy
Separate process on real UDP sockets adds delay, jitter, loss and a bottleneck
3 Linux kernel netem
Real kernel queues and loss on loopback, against kernel TCP
4 Two real machines
Laptops on different networks over the internet
Correctness: unit, end-to-end, handshake, file-integrity, chat and simulator tests (make test); packet parser fuzzed under AddressSanitizer and UBSan (make fuzz)
Statistics: paired seeds, 95% intervals, tuning seeds kept apart from test seeds
Every result has the command that produced it (docs/RUNNING_ALL_TESTS.md)

## Slide 22
ISSUES FOUND
What we found along the way
22 / 26
The first learned controller (a Q-table) was not faster than AIMD
At 10% random loss the neural agent was 7x slower than AIMD (85 s against 11 s)
Real sockets exposed a lost-handshake hang, spurious timeouts (262 retransmissions for about 3 losses) and a weak checksum
Our early baselines were weak: untuned AIMD (window cap 32) made first wins look bigger
Our own kernel tests were wrong four times: netem limit, untuned baseline, unequal payloads, synthetic 40-byte packets
The first BBR-style baseline stalled at 10% loss and took 163 s after a delay jump
The agent is a pushier neighbour than AIMD or CUBIC, and results vary with the training seed

## Slide 23
WHAT WE CHANGED
Every issue led to a fix
23 / 26
Before | After
Go-Back-N with a fixed 500 ms timer | Selective Repeat: bitmap ACKs, per-packet timers, adaptive timer with a 1.3 x srtt floor; about 10x fewer retransmissions
Byte-sum checksum | CRC-16: 0 of 333k corrupted packets accepted
Server ignored data after a lost final handshake ACK | Handled as in TCP, with a regression test
Q-table agent, window cap 32 | 5-32-32-5 neural network, cap 128, slow start, pacing
Neural agent 7x slower than AIMD at 10% loss | Hand-over to AIMD while loss is high: 13.9 s instead of 84.9 s
Untuned AIMD and CUBIC baselines | Tuned baselines, so every win is against a fair opponent
Faulty kernel and BBR tests | Netem limit, equal payloads and real 512-byte packets; kernel runs repeated; BBR stall and slow recovery fixed

## Slide 24
LIMITS
What we state openly
24 / 26
Kernel TCP is still 1.5x to 1.7x faster than the neural agent on every kernel path
Against tuned AIMD the agent takes about 70% of a shared link; the optional polite mode fixes that but costs speed
Level with CUBIC under bursty cross traffic; no gain at 10% random loss; the BBR-style baseline is faster on the 2% lossy path
Not formally verified: certified at +-0.001 for only 43% of decisions; trained in a simulator, never on real traces
Two-machine run: one drifting relay path, 4 of 20 runs timed out, so no ranking is claimed
Coexistence with kernel TCP: 3 runs per cell

## Slide 25
WRAP-UP
What we learned and what comes next
25 / 26
Learned
Reliability is a set of simple rules working together.
Congestion control matters as much as retransmission.
A tuned baseline is the only fair opponent.
Test tools fail in surprising ways, so check your own numbers.
Next
Controlled multi-machine tests on a direct network
Train with a competing flow so fairness is learned
Train on real traces with cross traffic
Close the gap to kernel TCP

## Slide 26
Thank you
github.com/Capsturrrr/replic
Harshavardhan Mallela Rohit Arya Shloak Sinha

## Slide 27
Neural agent in the C transport
Appendix Smart-REPLIC
1,200 packets, C transport | AIMD | Table (rl2) | Neural
5G-like | 1.38 s | 2.64 s | 1.18 s
Lossy wireless | 9.13 s | 7.54 s | 6.63 s
Satellite-like | 17.9 s | 38.1 s | 13.1 s
Neural agent beats AIMD on all three paths: 15%, 27%, 24% faster (95% intervals exclude zero)
Table agent does not generalise: slower on 5G-like and satellite-like
Selective ACK in C: about 10x fewer retransmissions, no significant time change here
Caveats: trained in a simulator; emulated paths (not real networks); agent retransmits more on random loss
15 runs per cell (satellite: 8), 95% intervals. Equal-cap check (AIMD capped at 32, 10 runs): neural still wins by 19%, 29%, 28%, all significant (eval_ci4.sh).

## Slide 28
Safety net: hand over to AIMD
Appendix Smart-REPLIC
C transport, seconds | AIMD 32 | Neural | Hybrid
5G-like | 1.48 | 1.17 | 1.23
Lossy 2% | 9.04 | 7.53 | 7.57
Satellite-like | 19.7 | 13.4 | 13.7
Hostile, 10% loss | 11.1 | 84.9 | 13.9
Problem found: at 10% loss the neural agent is 7x slower than AIMD
Fix: while a decision interval loses 10% or more, AIMD drives the window; after 3 clean intervals the agent resumes
Keeps the wins on the three benign paths, and the hostile path is no longer significantly different from AIMD
A timeout cut (x0.25) was tried and dropped: it helped the hostile path but hurt the 2% path (24 s vs 9 s)
Honest summary: the agent helps on clean-to-moderate paths; it needs a classical safety net elsewhere
10 runs per cell (hostile: 5 runs, 300 packets), 95% intervals. Flag: --hybrid 0.10. Code: eval_ci6.sh.

## Slide 29
More evidence: baselines, SACK, reordering
Appendix Smart-REPLIC
48 paths, original simulator | Mean | Median
Plain UDP | 68% delivered | -
TCP model (selective ACK) | 4.56 s | 1.48 s
REPLIC fixed window | 3.88 s | 2.00 s
REPLIC AIMD | 7.16 s | 2.72 s
Smart-REPLIC, table | 3.73 s | 1.99 s
Smart-REPLIC, deep | 3.20 s | 1.79 s
Selective ACK (simulated): AIMD mean 7.16 s to 4.90 s, median 2.72 s to 1.44 s; faster on 34 of 48 paths. Go-Back-N is the main weakness.
Reordering (20 ms jitter): AIMD 0.82 s to 6.79 s; deep agent 0.93 s; SACK removes most of the damage.
20-run intervals for the C experiments: Smart slower on 5G-like (+0.92 s) and satellite-like (+6.3 s), tie on lossy.
Caveat: this simulator allowed a dup-ACK retransmission storm. With the realistic rule, stress means are AIMD 7.75 s, neural 7.27 s: about level. The TCP row is a model, not kernel TCP.

## Slide 30
Fairness, ablations, chat fixes
Appendix Smart-REPLIC
Two flows, one bottleneck | Share of A | Jain
AIMD vs AIMD (long path) | 51% | 0.999
Deep vs deep (long path) | 59% | 0.969
Deep vs AIMD (no-loss path) | 44% | 0.987
Deep vs AIMD (long path) | 74% | 0.819
Fixed 8 vs AIMD (long path) | 72% | 0.843
Fair on short paths; takes 74% against AIMD on the 120 ms path, like a fixed window
Ablation: the no-shrink mask is what matters (6.54 s without it, about 3.3 s with it; AIMD 7.16 s)
Other parts (delay penalty, last action, throughput input) showed no measurable value
Same recipe gave 3.2 to 7.4 s across seeds: seed sensitivity is a real weakness
Found and fixed a dup-ACK retransmission storm in the chat gateway; added a live dashboard and an adaptive RTO
Simulator, 20 seeds; ablation on 48 stress paths. Code: web/fairness_test.py, web/ablate.py.

## Slide 31
Fairness and file transfer
Appendix Smart-REPLIC
Two flows, real sockets | Share A | Share B | Jain
AIMD vs AIMD | 49% | 51% | 0.99
Neural vs neural | 50% | 50% | 0.97
Neural vs AIMD tuned | 68% | 32% | 0.88
Neural vs AIMD cap 32 | 76% | 24% | 0.78
CUBIC vs AIMD tuned | 61% | 39% | 0.93
File transfer | AIMD cap 32 | AIMD tuned | Neural
2 MB, lossy 2% | 26.6 s | 24.2 s | 11.9 s
4 MB, fast path | 34.6 s | 21.0 s | 8.9 s
The agent is a more aggressive neighbour than AIMD or CUBIC: no starvation, but not polite. Not trained for fairness; TCP coexistence untested
smart_client --file sends a real file; the received file is byte-identical in every run (FNV-1a hash)
Terminal chat and web gateway now use the same 256-packet window and 32-byte bitmap as the C transport; interop test at 20% loss
CI, fuzzing, MIT licence, architecture doc

## Slide 32
Closing gaps: fairness and cross traffic
Appendix Smart-REPLIC
Neural vs tuned AIMD | Agent share | Jain
Default | 70% | 0.86
--polite 1.2 | 49% | 0.95
--polite 1.3 | 52% | 0.94
--polite 1.5 | 59% | 0.90
Bursty cross traffic | Time | vs AIMD
AIMD tuned | 5.73 s | 1.00
CUBIC tuned | 4.55 s | 0.79
Neural agent | 4.87 s | 0.85
Neural, polite 1.3 | 4.92 s | 0.86
Polite mode: back off when a standing queue builds (jitter-aware). Share 70% to 52%; costs speed (0.53x to 0.58x of AIMD time on 100 paths, worst path 2.95x slower), so it is off by default
Bursty cross traffic (new proxy option, 8 runs): neural is 15% faster than tuned AIMD but level with CUBIC; three tweaks to fix its extra retransmissions did not help
Server now handles up to 16 clients at once; a test sends two files simultaneously and checks both byte-for-byte

## Slide 33
Real sockets found what the emulator could not
Appendix Smart-REPLIC
Lost handshake ACK
Server ignored all data after a lost final ACK: transfers hung (2 of 4 runs at 10% loss). Fixed as in TCP; regression test added.
Spurious timeouts
Timer too tight for window bursts: 262 retransmissions for ~3 losses. Floor of 1.3 x srtt. It also made AIMD 41% faster, so the old margins were too big.
Weak checksum
Byte-sum checksum let 2% of corrupted packets through (fuzzer). Now CRC-16: 0 of 333k accepted, sanitizers clean.
Independent check on real UDP sockets through an impairment proxy (src/impair.c): neural agent -17% / -53% / -45% / -39% vs tuned AIMD on 5G / lossy / satellite / fast; hostile path a tie. eval_proxy.sh

## Slide 34
Problems we hit and fixed
Appendix Smart-REPLIC
Problem | Fix
Server stuck after killed client | Accept SYN in any state (was a 15.5 s hang)
Leftover netem rule | Check tc qdisc show dev lo, delete before each test
Windows Wireshark saw nothing | Capture with tshark inside WSL, then copy
Shell portability in benchmark | Replaced date/grep tricks with awk and sed

## Slide 35
Our first learned agent: an honest result
Appendix Smart-REPLIC
6 evaluation runs per scenario after 40 training episodes
Not faster: +63% time on 5G-like, +10% on satellite, tie on lossy
Fewer retransmissions on 5G-like and satellite, but within run-to-run noise
Earlier training rounds were much worse; reported run is the final configuration

## Slide 36
Benchmark results
Appendix Smart-REPLIC
62 of 62 packets delivered at every loss level, from 0% to 40%.

## Slide 37
Literature behind the design
Appendix Smart-REPLIC
Jacobson & Karels (1988): congestion avoidance and control, the origin of AIMD
Chiu & Jain (1989): why additive increase, multiplicative decrease converges fairly
RFC 5681 (2009): TCP congestion control standard
Ha, Rhee, Xu (2008): CUBIC, our future-work direction
Langley et al. (2017) and RFC 9000: QUIC, reliable transport over UDP in production
Midhula & Arun Raj Kumar (2024) and Cao et al. (2023, DRLFcc): deep reinforcement learning for congestion control, the idea behind Smart-REPLIC
Key researcher: Van Jacobson

## Slide 38
Smart-REPLIC: a Q-learning window controller
Appendix Smart-REPLIC
State (80)
RTT ratio x loss fraction x window size, sampled once per RTT.
Action (5)
Multiply cwnd by 0.5, 0.85, 1.0, 1.15 or 1.5.
Reward
Throughput gained, minus delay growth, minus retransmissions.
Same Go-Back-N reliability as the baseline; only the window policy changes. Paths emulated in-program: 5G-like, lossy wireless, satellite-like.

## Slide 39
The AI agent in our code
Appendix Smart-REPLIC
src/rl_cc.h (agent, simplified)
// state: 4 x 4 x 5 = 80 buckets
s = (rtt_bucket*4 + loss_bucket)*5 + cwnd_bucket;
// choose: explore with prob. eps, else best
int rl_choose(a, s) {
if (rand01() < a->eps) return rand() % 5;
return argmax(a->q[s]); // 5 actions
}
// learn: the Q-learning update
void rl_update(a, s, act, r, s2) {
target = r + a->gamma * max(a->q[s2]);
a->q[s][act] += a->alpha * (target - a->q[s][act]);
}
src/smart_client.c (decision loop, simplified)
// once per RTT, in smart_client.c
ratio = rtt / base_rtt; lossf = losses / sent;
reward = sqrt(throughput_norm)
- 0.5 * max(0, ratio - 1) // delay growth
- 4.0 * lossf; // loss
rl_update(&ag, prev_s, prev_a, reward, s2);
act = rl_choose(&ag, s2);
cwnd *= {0.5, 0.85, 1.0, 1.15, 1.5}[act];
Tabular Q-learning: alpha 0.15, gamma 0.9. Chat version: web/cc.py, trained in web/train.py (results/q_chat.txt). Deep version: web/dqn.py, a small neural network (5-32-32-5) trained by DQN in web/train_deep.py.

## Slide 40
Appendix: slow start and congestion avoidance
Appendix Smart-REPLIC
cwnd starts at 1
+1 per ACK until ssthresh = 16
Then +1/cwnd per ACK
62 packets, final cwnd 18.71